## Slide 1
Town of Branford, Connecticut | May 3, 2016
TOWN OF BRANFORD
COASTAL RESILIENCE PLAN
Presentation of the Plan
Janice Plaziak, P.E., Town of Branford
David Murphy, P.E., CFM, Milone & MacBroom, Inc.
Scott Choquette, CFM, Dewberry

## Slide 2
Presentation Agenda
Plan Overview
Review
  Resilience
  Adaptation
Recommendations
  Townwide
  Access
  Region-Specific
Planning Examples
  Neighborhood Concepts
  Infrastructure Designs
Conclusions
Next Steps
Discussion
Review
Recommend
Discussion
Plan
Townwide
Access
Region
Conclusions
Next
Plans

## Slide 3
The Plan: Where we Are
Done
Review Existing Capabilities
Coordinate with “Regional Framework”
Data Collection
Vulnerability and Risk Assessment
Public Information Meetings, Surveys
Select Sandy-Impacted Neighborhoods
Coastal Resilience Plan
Implementation Plan and Process
Spring
Winter
Winter
Now
Now
Done
Done
Done
Spring
Conceptual Designs
Review of Adaptation Options
Review
Recommend
Discussion
Plan
Townwide
Access
Region
Conclusions
Next
Plans
Notes: Coastal Resilience Plan Document
  Combinations of coastal hazard mitigation, adaptation, and resilience solutions at the locations that are highlighted in Task 7, as well as strategies and actions for the entire town

## Slide 4
The Plan
Review
Recommend
Discussion
Plan
Townwide
Access
Region
Conclusions
Next
Plans

## Slide 5
Review: Resilience
Community Capacity
Initial Greatest Loss
Time 
Event!
Greatest Loss
Improved
Recovery
Prepare
Initial
Recovery
Faster Recovery
Withstand Less Damage
Prepare
Adapt
Withstand
Recover
Reduce Recovery Time
Decrease Damage
Increase Capacity
Review
Recommend
Discussion
Plan
Townwide
Access
Region
Conclusions
Next
Plans

## Slide 6
Review: Adaptation
IPCC: 3 Approaches (1990)
Retreat
Accommodation
Protection
NOAA 7 Categories (2010)
Identify and Assess Impacts
Awareness and Assistance
Manage Development
Reduce Losses
Manage Shoreline
Manage Coastal Ecosystem
Manage Water Resources
Regional
Scale
Site-Specific Scale
Review
Recommend
Discussion
Plan
Townwide
Access
Region
Conclusions
Next
Plans

## Slide 7
Recommendations
Category | Specific Options
Hard Protection | Seawalls
 | Bulkheads
 | Revetments
 | Dikes
 | Groins
 | Breakwaters
Soft Protection | Beach Nourishment
 | Dune Restoration
Hybrid Protection | Bioengineered Banks
 | Artificial Reefs
Infrastructure | Drainage Improvements
 | Road Elevation
 | Wastewater Treatment Plant Floodproofing
 | Sewer Pumping Station Floodproofing
 | Community Wastewater
 | Strengthen Power Utilities
 | Tide Gate Maintenance
Home Protection | Elevation
Regulatory Tools | Flood Damage Prevention : Freeboard V zone standards in Coastal A zones
 | Zoning Modifications: Height Limit Flexibility Reconstruction Flexibility
Coastal Realignment | Road Retirement
 | Alternate Egress Development
 | Property Acquisitions
Review
Recommend
Discussion
Plan
Townwide
Access
Region
Conclusions
Next
Plans

## Slide 8
2020’s Daily
2080’s Daily
Sea Level Rise Scenarios
2080’s Cat. 2
2050’s Daily
2020’s Cat. 2
Recommendations: Townwide
Review
Recommend
Discussion
Plan
Townwide
Access
Region
Conclusions
Next
Plans

## Slide 9
Recommendations: Townwide
2020’s Daily
2080’s Daily
Sea Level Rise Scenarios
2080’s Cat. 2
2050’s Daily
2020’s Cat. 2
 | Shoreline Protection |  |  |  |  | Infrastructure |  |  |  |  |  | Structure |  | Realignment |  | 
 | Hard Protection | Beach Nourishment | Dune Restoration | Living Shoreline | Bioengineered Banks | Drainage | Pumping Station | Community Wastewater | Power Utilities | Road Elevation | Tide Gates | Structure Elevation | Floodproof Structures | Alternate Routes | Property Acquisition | Road Retirement
Clark Ave | X | X |  |  |  |  | X |  | X | X |  | X |  |  | X | 
Beckett Beach | X | X |  |  |  | X | X |  | X | X | X | X |  |  | X | 
Short Beach | X | X |  | X | X |  | X |  | X | X |  | X |  |  | X | 
Killams Point |  |  |  |  |  |  |  |  | X | X |  |  |  | X |  | 
Johnsons Point |  |  |  |  |  |  |  |  | X | X |  |  |  |  | X | 
Double Beach | X | X |  | X | X |  | X |  | X |  |  | X |  |  | X | 
Branford Point |  |  |  |  |  |  | X |  | X | X |  | X | X |  |  | 
Branford Center | X |  |  |  |  | X | X |  | X | X | X | X | X |  |  | 
Blackstone Acres | X |  |  |  |  | X | X |  | X | X | X | X |  |  |  | 
Indian Neck Ave |  |  |  |  |  |  |  |  | X | X |  | X |  |  |  | X
Sybil Creek |  |  |  |  |  |  | X |  | X | X | X | X |  |  | X | 
Pawson Park |  |  |  |  |  |  | X |  | X | X | X | X |  |  |  | 
Linden Ave | X |  |  | X | X |  | X |  | X |  |  |  |  |  |  | 
Limewood Ave | X | X | X |  |  |  |  |  | X | X |  | X |  |  | X | 
Haycock Point | X |  |  |  |  |  |  |  | X |  |  | X |  |  |  | 
Hotchkiss Grove | X | X | X |  |  | X | X |  | X |  |  | X |  |  | X | 
Pine Orchard | X | X |  |  |  |  |  |  | X | X | X | X |  |  |  | 
Juniper Point |  |  |  |  |  |  |  |  | X | X |  |  |  |  |  | 
Pleasant Point |  |  |  |  |  |  |  | X | X | X |  |  |  |  |  | 
Stony Creek | X | X |  |  |  | X |  | X | X |  | X | X | X | X |  | 
Jarvis Creek |  |  |  |  |  |  |  |  | X | X | X |  |  |  |  | 
Review
Recommend
Discussion
Plan
Townwide
Access
Region
Conclusions
Next
Plans

## Slide 10
Recommendations: Townwide
2020’s Daily
2080’s Daily
Sea Level Rise Scenarios
2080’s Cat. 2
2050’s Daily
2020’s Cat. 2
Townwide Regulatory Changes | 
TR1 | Relax 35-ft height restriction to facilitate elevation
TR2 | Adopt freeboard that exceeds State-recommended one foot
TR3 | Apply V zone standards in coastal A zones
TR4 | Require that developers removing fill within the coastal zone analyze changes that will have on flood risk and NFIP status
TR5 | Increase Townwide tree and limb maintenance
Townwide Promotion of Property Protection | 
PP1 | Partner with property owners to apply for grants to elevate homes
PP2 | Promote Shore Up and similar home elevation loan programs
PP3 | Encourage homeowners to consider having the Town acquire their property
Municipal Wastewater System | 
WW1 | Floodproof the Wastewater Treatment Plant
WW2 | Elevate or Floodproof Vulnerable Sewer Pumping Stations, including: Beckett Avenue Little Bay Lane Pages Central (Meadow St) Riverside Drive (Blackstone) Blocks Sybil (@ 146) Summer Island Hotchkiss Grove Clark Avenue Johnsons Point Branford Point Frank Street
Review
Recommend
Discussion
Plan
Townwide
Access
Region
Conclusions
Next
Plans

## Slide 11
2020’s Daily
2080’s Daily
Sea Level Rise Scenarios
2080’s Cat. 2
2050’s Daily
2020’s Cat. 2
Recommendations: Access
State Routes | 
1 | 146 @ Jarvis Creek
2 | 142 @ Short Beach
3 | 146 @ Sybil Creek
4 | 146 @ Branford River
5 | 146 @ Limewood Beach
6 | 1 @ Branford River
7 | 146 @ Stony Creek
8 | 142 @ Beckett Beach
9 | 142 @ Stannard Avenue
Town Roads | 
1 | Linden Ave
2 | Indian Neck Ave
3 | Waverly Park Rd
4 | Pine Orchard Rd
5 | Clark Ave
6 | Thimble Island Rd
7 | Harbor St
8 | Woodvale Rd
9 | Johnsons Point Rd
10 | Killams Point Rd
11 | Spring Rd
12 | Maple St
13 | Main St
14 | Ark Rd
15 | Pleasant Point Rd
16 | Pawson Rd
17 | Totoket Rd
18 | Grove St
19 | Stannard Ave
Review
Recommend
Discussion
Plan
Townwide
Access
Region
Conclusions
Next
Plans

## Slide 12
Recommendations: Regional
Stony Creek Neighborhood | 
SC1 | Fortify Trolley Trail Bridge abutments
SC2 | Develop evacuation plan
Beckett Avenue Beach | 
BB1 | Retrofit drainage systems
BB2 | Beach nourishment
BB3 | Encourage property elevation
Jarvis Creek | 
JC1 | Assist/support resolution of tide gate problems
Short Beach | 
SB1 | Upgrade drainage system
Killams Point | 
KP2 | Construct alternative egress to Turtle Bay Drive
KP3 | Killams Point Conference Center emergency and evacuation plans
Johnsons Point | 
JP2 | Upgrade Spring Road bridge
Double Beach | 
DB1 | Stabilize Lanphier Cove bank
DB2 | Pursue acquisition of VE zone properties
DB3 | Reroute sewer infrastructure over time
Meadow Street/Hammer Field | 
MS1 | Automatic flood gate at underpass
MS2 | Upgrade drainage system
MS3 | Elevate railroad berm over time
MS4 | Ensure substation protection
MS5 | Consider emergency shelter status
Downtown Area | 
DT1 | Upgrade Village Green Court drainage
Blackstone Acres | 
BA1 | Floodwalls to protect from future high tides
BA3 | Stormwater pumping-station
BA4 | Levee to protect from storm surge
Indian Neck Avenue Area | 
IN1 | Abandon Tabor Road section
Sybil Creek | 
SC1 | Install / improve tidegate
SC3 | Home elevation on Waverly Road
SC4 | Pursue property acquisitions
Pawson Park | 
PP1 | Linden Avenue Bank Stabilization near Bayberry Lane
PP2 | Linden Avenue Bank Stabilization near Old Pawson Road
PP3 | Upgrade Linden Avenue drainage systems
PP3 | Develop evacuation plan
Limewood Avenue | 
LA1 | Stabilize Route 146
LA2 | Beach nourishment
LA3 | Dune enhancement
Hotchkiss Grove | 
HG1 | Identify where dunes and walls can be used together for flood and storm surge protection
HG2 | Retrofit drainage system
HG3 | Consider Beach Nourishment
Pine Orchard | 
PO2 | Beach nourishment
Review
Recommend
Discussion
Plan
Townwide
Access
Region
Conclusions
Next
Plans

## Slide 13
Examples for Planning
Meadow Street
And
Hammer Field
Blackstone
Acres
Lanphier Cove
Review
Recommend
Discussion
Plan
Townwide
Access
Region
Conclusions
Next
Plans

## Slide 14
Examples: Meadow Street and Hammer Field
Review
Recommend
Discussion
Plan
Townwide
Access
Region
Conclusions
Next
Plans

## Slide 15
Existing Conditions
Abandon Opening
Flood Gate
Examples: Meadow Street and Hammer Field
Review
Recommend
Discussion
Plan
Townwide
Access
Region
Conclusions
Next
Plans

## Slide 16
Examples: Meadow Street and Hammer Field
2080s DHT
gate closed
2080s DHT
gate open
Review
Recommend
Discussion
Plan
Townwide
Access
Region
Conclusions
Next
Plans

## Slide 17
2050s
Category 2
Gate Closed
2080s
Category 2
Gate Closed
Examples: Meadow Street and Hammer Field
Review
Recommend
Discussion
Plan
Townwide
Access
Region
Conclusions
Next
Plans

## Slide 18
Examples: Blackstone Acres
Review
Recommend
Discussion
Plan
Townwide
Access
Region
Conclusions
Next
Plans

## Slide 19
2080s No Storm
Examples: Blackstone Acres
Floodable Neighborhood
Wall-Protected
Berm-Protected
Review
Recommend
Discussion
Plan
Townwide
Access
Region
Conclusions
Next
Plans

## Slide 20
Examples: Blackstone Acres
Floodable Neighborhood
Wall-Protected
Berm-Protected
2080s Category 2 Storm
Review
Recommend
Discussion
Plan
Townwide
Access
Region
Conclusions
Next
Plans

## Slide 21
Examples: Meadow Street
Review
Recommend
Discussion
Plan
Townwide
Access
Region
Conclusions
Next
Plans

## Slide 22
Examples: Lanphier Cove
Review
Recommend
Discussion
Plan
Townwide
Access
Region
Conclusions
Next
Plans

## Slide 23
Concepts: Lanphier Cove
Review
Recommend
Discussion
Plan
Townwide
Access
Region
Conclusions
Next
Plans

## Slide 24
Concepts: Lanphier Cove
Review
Recommend
Discussion
Plan
Townwide
Access
Region
Conclusions
Next
Plans

## Slide 25
Conclusions
Branford has the capacity to decrease vulnerabilities and therefore decrease risks
From daily high tide flooding, storm surges, erosion, and sea level rise
Branford can adapt
At the Town, neighborhood, and parcel scale
Utilities & infrastructure can be strengthened
Access can be maintained
Beaches and dunes can be nourished/restored
Drainage can be upgraded
Homes will continue to be elevated
Residents can relocate if desired
Branford has the capacity to increase its Resilience
Prepare, Adapt, Withstand, Recover
Short Beach
Image: greencitiesbluewater.wordpress.com
Short Beach
Image: Geoffrey Booth, DiegeticShadow
Review
Recommend
Discussion
Plan
Townwide
Access
Region
Conclusions
Next
Plans

## Slide 26
Next Steps
Review the Draft Plan
Provide Input
Prepare Final Document
City has options for formalizing the plan:
  Adopt as a stand-alone plan
  Accept as a working/living document to be maintained by a commission or board
  Append to Hazard Mitigation Plan
  Append to Plan of Conservation and Development
Implementation
  Execute existing grants from FEMA
  Keep securing grants from FEMA along with CIRCA, NOAA, and others
  Become more resilient!
Review
Recommend
Discussion
Plan
Townwide
Access
Region
Conclusions
Next
Plans

## Slide 27
Discussion
Stony Creek
Image: Mary Johnson Photography 2011
Review
Recommend
Discussion
Plan
Townwide
Access
Region
Conclusions
Next
Plans